## Slide 1: Probabilistic Seismic Hazard Assessment of North Africa: a GEM's Product
Valerio Poggi, Julio Garcia, Richard Styron, Robin Gee
Global Earthquake Model (GEM), Pavia Italy
36th General Assembly of the
European Seismological Commission
September 3rd, 2018, Valletta - Malta

## Slide 2: Introduction to GEM
the construction of a global mosaic of open hazard models
to provide the community with tools (such as OpenQuake), datasets and knowledge to achieve this goal
GEM (Global Earthquake Model) is a no-profit organization funded by public and private partners aimed to stimulate the awareness on seismic hazard and risk worldwide
The overall goal of the hazard component of the GEM community is:

## Slide 3: GEM Global Database of Hazard Models
The DB contains hazard models developed by national agencies and international projects which are openly distributed
SSAHARA Project
SARA
Project
RESIS 2
Project
NAF18
NWA18

## Slide 4: Earthquake Hazard in North Africa
Besides the East African Rift System, significant seismicity also occurs along a wide belt bounding the Mediterranean coastline
Several past large earthquakes caused a non-negligible level of damage
A reliable risk assessment is therefore essential, which requires a state-of-art hazard assessment for the region
There is a need for a new probabilistic seismic hazard model based on the most recent and up to date available information
NAF18

## Slide 5: North Africa Homogenized Earthquake Catalogue
The catalogue is obtained by harmonization of global bulletins with data from local agencies and published studies
Mw
Number of Events: 5170
Year Rage: 1016 - 2013
Magnitude Rage: 4.0 - 8.5
ISC-GEM
ISC Reviewed
GCMT
IGN
GEM-GHEC
EMEC
Literature

## Slide 6: Source Model - Regional Seismicity Analysis
Earthquake
Source Zones
Hypocentral Depth
Distribution
Magnitude-Frequency
Analysis
Rupture Mechanism
Identification

## Slide 7: Occurrence Rate Redistribution
We have implemented a smoothing procedure based on area source zonation, where the observed rates (R) are spatially redistributed according to the seismicity pattern of the area, while keeping the overall rate balance unmodified:

## Slide 8: Global Active Fault Database
New database of active faults from Morocco to Sinai
143 structures mapped from literature, satellite imagery, topography, seismicity
Slip taken from literature or estimated from GPS
Public and open-source (Creative Commons Attribution license)

## Slide 9: Tectonic Regionalization using Fuzzy Logic
Chen et al. 2017
Merging information from:
Seismicity (magnitude)
Smoothed Moment rate
S-wave velocity
QLG distribution
Group A
Group B

## Slide 10: GMPE Selection and Logic-Tree Approach
Chiou & Youngs (2014)
Akkar et al. (2014)
Atkinson & Boore (2006)
Pezeshk et al. (2011)
 Active Shallow Crust (Group A)
 Stable Continental Crust (Group B)
Given the peculiar seismoteconic setting of the North Africa, an hybrid attenuation behavior might be expected. Four suitable GMPEs have been selected:
Three main tectonic groups are then identified, each with a different GMPE weighting scheme
Logic Tree

## Slide 11: GMPE Selection – Comparing Ground Motion
Distance (rjb)
Magnitude
Selection needs verification with empirical data….

## Slide 12
1 station in Morocco: 8 Events available
(6 usable)
2 stations in Algeria: 2 Events
Need data from local agencies (e.g. CRAAG) or neighboring countries

## Slide 13: Preliminary Hazard Results
10% POE in 50 years (0.2s)
Fault Source Model
Smoothed Seismicity Model
Area Sources (Background)
+

## Slide 14: Hazard Curves @ African Capitals
Morocco
Algeria
Tunisia
Egypt

## Slide 15: Uniform Hazard Spectra @ African Capitals
10% POE in 50 years
Morocco
Algeria
Tunisia
Egypt

## Slide 16: Model Verification: Stochastic Ruptures
Stochastic earthquake catalogue for a 10.000 years investigation time
Relevant sources have been considered for verification
Sampling of the full logic-tree
All ruptures with Mw>4.5
Zone 3 – Cumulative MFD
Smoothed
Background
Catalogue MPD

## Slide 17: GEM Global Mosaic of Hazard Models
PRELIMINARY
PRELIMINARY

## Slide 18: Missing Components / Improvements
The North-Africa Hazard model is presently just in a GEM product, but it is meant to be improved and expanded with the collaboration of the African and worldwide scientific community
While existing components can be improved, many other components are still missing, such as:
Integration of local hazard studies
Strong motion recordings from local networks
Site-specific studies and microzonation
Need for a collaborative effort

## Slide 19
  Except where otherwise noted, this work is licensed under https://creativecommons.org/licenses/by-nc-nd/3.0/
  Please attribute to the GEM Foundation with a link to
  www.globalquakemodel.org
Thank you!

## Slide 20: OpenQuake Engine - GitHub repository

## Slide 21: OpenQuake Engine – QGIS integration
From/To
OpenQuake
Source
Model

## Slide 22: OpenQuake Engine – QGIS integration (2)

## Slide 23: GEM Global Database of Hazard Models
http://platform.openquake.org
http://hazardwiki.openquake.org